Bleeding Hydraulic System

BE VERY CAREFUL WHEN BLEEDING SYSTEM AROUND MOVING PARTS.

This procedure will work much easier with 2 people:

- Fill upper cylinder with oil

- Start lathe; crack hydraulic hose at lower pulley cylinder.

- With the lathe running, slowly turn to high speed, just before reaching high speed, close hydraulic hose on lower pulley cylinder.  Turn to low speed.

- Stop the lathe and start at # 1 again.

- You may need to repeat this process a dozen times before all the air is bled from the system.